## Slide 1: Fuel Properties AEN/TSM 220
Properties
Estimating Performance
Ignition Properties – Octane/Cetane
Engine Efficiency

## Slide 2: Fuel Properties
Energy content – BTU or kJ
Energy density – energy/vol OR energy/mass
Physical density – mass/vol
Ignition Properties – Octane/Cetane
Flowability (viscosity)

## Slide 3: Energy Density
Calorie: heat required to raise the temperature of one gram of water one degree Celsius.
Joule:
BTU: heat required to raise the temperature of one pound of water one degree Fahrenheit.
Energy density:

## Slide 4: Typical SI Fuels
 | Gasoline | E85 | Ethanol
Energy Density (BTU/gal) | 115000 (32000 kJ/L) | 82000 (22900 kJ/L) | 76000 (21200 kJ/L)
Density (lb/gal) | 6.1 | 6.4 | 6.5
Octane | 87 – 95 | 105 | 117
Blends up to 10% for oxygenator (MTBE replacement)
E85 supply availability

## Slide 5: CI Fuels
 | No. 2 Diesel | Pure Biodiesel
Energy density (BTU/gal) | 129,000 (36000 kJ/L) | 118,000 (32900 kJ/L)
Physical density (lb/gal) | 7.08 | 7.33
Cloud point (F) | 5 - 41 | 27 - 54
Cetane | 40 - 55 | 48 - 65
Typical blends are B5 or less
Need additives for cold weather
Biodiesel adds lubricity (Replaces Sulphur)

## Slide 6: Fuel Properties AEN/TSM 220
Properties
Estimating Performance
Ignition Properties – Octane/Cetane
Engine Efficiency

## Slide 7: Estimating Performance Differences
A tractor gives a maximum power of 75 hp using petroleum diesel fuel. Approximately how much power would it produce if we used pure biodiesel?

## Slide 8: Fuel Economy
 | E85 | Gasoline
MPG (city) | 13 | 18
MPG (highway) | 18 | 24
2017 Ford F-150 www.fueleconomy.gov

## Slide 9: Fuel Properties AEN/TSM 220
Properties
Estimating Performance
Ignition Properties – Octane/Cetane
Engine Efficiency

## Slide 10: Octane/Cetane
Quantifies autoignition properties of fuel
Octane (Gasoline/Ethanol)
  Higher octane = higher ignition pressure
Cetane (Diesel)
  Higher cetane = lower ignition pressure

## Slide 11: Octane/Cetane Implications
Not related to energy content!
Higher Octane means:
  Higher autoignition pressure
  Higher compression ratio possible
  Less knock and “dieseling”
  Cleaner burn
Higher Cetane means:
  Lower autoignition pressure
  Less low RPM knock
  Better cold starting
  Maybe higher emissions????

## Slide 12: Fuel Properties AEN/TSM 220
Properties
Estimating Performance
Ignition Properties – Octane/Cetane
Engine Efficiency

## Slide 13: Efficiency
Ex: John Deere 6220 tractor uses 4.85 gal/hr of diesel fuel while producing 75.8 hp. Find the efficiency.

## Slide 14
Ex: CaseIH Maxxum 125 uses 26.37 L/hr while producing 85.6 kW of power. Find the efficiency.